## Slide 1: Summer Project
Synthesize and Place and Route a OpenCore Risc V design
Risc V https://riscv.org/
  Competition to the ARM core
  Improvements intended over ARM since it is a new design
  Not just an educational core, but one intended for industry use
    https://www.sifive.com/ is building a company around Risc V
  Open Source so no royalties
What to be done as a team
  Get the RTL and synthesize using Synopsys 28nm library
  Generate any memories using Synopsys Memory Compiler
  Place and route the database
  Add any extra components like caches that make sense
  Add Ios to make it like a stand alone chip
  Implement all phases of the flow
  Possibly implement in FreePDK and OpenRam to not be tied to Synopsys library
Meet once a week through email or in person
  Set weekly goals
  Could be done as a credit, but we would need to work out the logistics
  Great for learning and the resume
Other possible cores:
  https://opencores.org/, https://openrisc.io/, http://nvdla.org/, https://github.com/VerticalResearchGroup/miaow/wiki

## Slide 2: Current Team
Zoe Zhang
Shubham Mathur: syn/auto
Saida Akhter: syn/auto
Saranya Kannan: Mem
Pialy Barua
Hima Ethakota
Niranjan Anbarasu: syn
Rezwana Mahbub: syn/auto
Kishore Sudini: Guide
Deepu Manjegowda?
Leo Diaz:Mem
Suddha Talukdar
Mohan Maduri: git/Mem
Ataur Patwary
Brian Cruikshank
Zeba Khan: auto

## Slide 3: Break into subteams
Working on memories?
Working on initial synthesis/APR?
Working on automation scripts?
  Github? Documentation? listserv?

## Slide 4: 2 Cores to work with
Rocket-chip (in order core plus surrounding logic)
  Also designed for use with FPGAs
  SiFive is doing work here and in other spots
  Roy Kravitz is working with SiFive to get a Risc V FPGA setup for the other classes.
  Can we download these or similar version to Diligent Nexys A7-100T?
Boom (out of order core and reuses Rocket-chip surrounding logic)
  Larger core and probably more interesting for larger VLSI work
  Maybe more interesting to partition
  https://content.riscv.org/wp-content/uploads/2017/12/Wed0936-BOOM-v2-An-Open-Source-Out-of-Order-RISC-V-Core-Celio.pdf
  Could this or a reduced version fit on FPGA?
Both need memories to be set up
Both have lots of pins on their top level, so maybe not good for Full Chip as is
  How to change this?

## Slide 5: Getting started
Use mo.ece.pdx.edu
  Transfer files from eve using /home/$USER/common or Documents subdirectory
Addpkg: use synopsys-icc2017, synopsys-icv2017, synopsys-2019_06
  remove others
Add lines to .bashrc, Have .bash_profile source .bashrc
  export RISCV='/pkgs/riscv/riscv-tools'
  PATH="$RISCV/bin:$PATH"
  PATH="/pkgs/riscv/misc-bin/bin:$PATH"
  PATH="/pkgs/riscv/misc-bin/jdk-12.0.1/bin:$PATH"
  PATH="$PATH:/pkgs/synopsys/I-2013.12-SP1/amd64/syn/bin"
  export ICV_HOME_DIR="/pkgs/synopsys/2017/ic_validator"
RTL locations
  /pkgs/riscv/rocket-chip/vsim/generated-src
  /pkgs/riscv/boom-template/vsim/generated-src
Scala example (but don’t dig here too much. Other items more important)
  /pkgs/riscv/rocket-chip/src/main/scala/tile/
Think about perfecting scripts for syn/apr/pt
Initial floorplan boundary can be left open to the tool
Getting RFs worked out. black box for now?
Github? ListServ? Documentation?

## Slide 6: Getting Memories working
Leave the memory module as a black box for now.
May need to don’t_touch to make items not optimized out.
Use the memory compiler to generate new ones that will work.
  /pkgs/riscv/NOTES has information on this
Use existing memory combinations in libraries to work
  /pkgs/riscv/NOTES has information on this
Memories will not exactly fit needs. You will need to combine or make larger.
Physical Register file on Boom was a challenge for Berkeley. Try their solution after everything else figured out.
  RegisterFileSynthesizable(
    3 read, 2 write (floating point)
  RegisterFileSynthesizable_1(
    6 read, 3 write (Integer)

## Slide 7: Building Boom & Rocket-Chip
It took a while to get it to build
Many packages update/install
  automake-1.15 bison-3.4.1 flex-2.6.4 libtool-2.4 pkg-config-0.29.2 texinfo-6.6 jdk-12.0.1 dtc-1.5.0
Some compile/link variables to update
Most work and disk space for /pkgs/riscv/riscv-tools/
  Probably not need to have locally. Just point to it if needed.
The other parts are not as bad or large.
Notes in /pkgs/riscv/NOTES

## Slide 8: Potential Automation Scripts
psu-pd-scripts/
start up script for each tool. stage started by running a command? Or use Make?
syn.tcl (variables for design name, other files for sdc, upf, border, blockages)
add_ios.tcl
partition.tcl
apr.tcl (variables for design name and what to run?)
apr-import-floorplan.tcl
apr-place.tcl
apr-cts.tcl
apr-route.tcl
pt.tcl (run a corner or setup/hold depending on variables or procedure parameters)
pt-dmsa.tcl
lib-load (depending on variables or procedure parameters) for syn/apr/pt

## Slide 9: Potential Work Structure
scripts/
syn/
    work
    outputs
    reports
apr/
    work
    outputs
    reports
pt/
    work
    outputs
    reports
    constraints/ (sdc, upf, border, pin-placements, blockages, path groups, macro placements. Standard names involving the design name)
rtl/

## Slide 10: Interesting RiscV Videos and links
Ihttps://content.riscv.org/wp-content/uploads/2017/12/Wed0936-BOOM-v2-An-Open-Source-Out-of-Order-RISC-V-Core-Celio.pdf
Videos on Boom
2015: https://www.youtube.com/watch?v=z8UInbiQbdA
2016: https://www.youtube.com/watch?v=JuJDPbzWpR0
2017: https://www.youtube.com/watch?v=toc2GxL4RyA
About riscV
https://www.youtube.com/watch?v=GWmo8y-eR0c
https://www.youtube.com/watch?v=NTMxZgoBp84
riscv isa vs others:
https://www.youtube.com/watch?v=Ii_pEXKKYUg
Boom documentation on how the Core Processor works
https://docs.boom-core.org/en/latest/
Good reference books:
Computer Architecture: A Quantitative Approach
Modern Processor Design: Fundamentals of Superscalar Processors
Git Clones for Builds
git clone https://github.com/ucb-bar/rocket-chip.git
git clone https://github.com/riscv-boom/boom-template.git
Mentions making a fpga and vlsi version of rocket chip: https://github.com/freechipsproject/rocket-chip